enum{Idle,Counting,
int current = Idle;
#define G1 A0
#define G2 A1
#define G3 A2
#define G4 A3
#define Y1 A4
#define Y2 A5
#define R1 3
#define R2 4
int ES = 6;
int XS = 7;
int count;
// Step1. Created for the input signal, prevName, currName.
int prevESstat = 0;
int currESstat = 0;
int prevXSstat = 0;
int currXSstat = 0;
void setup()
{
  Serial.begin(9600);
  pinMode(G1, OUTPUT);
  pinMode(G2, OUTPUT);
  pinMode(G3, OUTPUT);
  pinMode(G4, OUTPUT);
  pinMode(Y1, OUTPUT);
  pinMode(Y2, OUTPUT);
  pinMode(R1, OUTPUT);
  pinMode(R2, OUTPUT);
  pinMode(ES, INPUT);
  pinMode(XS, INPUT);
}
void output(int G1Value, int G2Value, int G3Value, int G4Value, int Y1Value, int Y2Value, int R1Value, int R2Value)
{
  digitalWrite(G1, G1Value);
  digitalWrite(G2, G2Value);
  digitalWrite(G3, G3Value);
  digitalWrite(G4, G4Value);
  digitalWrite(Y1, Y1Value);
  digitalWrite(Y2, Y2Value);
  digitalWrite(R1, R1Value);
  digitalWrite(R2, R2Value);
}
void loop()
{
  //Step 2. Read current before load
  currESstat = digitalRead(ES);
  currXSstat = digitalRead(XS);

  switch(current){
    case Idle:
    Serial.println("Idle");
    output(0,0,0,0,0,0,0,0);
    count = 0;
    delay(100);
        current = Counting;
    break;
    case Counting:
    Serial.println("Counting");
    Serial.println(count);
    if (prevESstat == 0 && currESstat == 1){
          count++; //count = count+1
          current = Counting;
    }
    if (prevXSstat == 0 && currXSstat == 1){
          if (count > 1){
            count--; //count = count-1
            current = Counting;
          }
    }
    if((prevESstat == 0 && currESstat == 1 && count == 1)||(prevXSstat == 0 && currXSstat == 1 && count == 1)){
          current = Having1Person;
        }
    if((prevESstat == 0 && currESstat == 1 && count == 2)||(prevXSstat == 0 && currXSstat == 1 && count == 2)){
          current = Having2Persons;
        }
    if((prevESstat == 0 && currESstat == 1 && count == 3)||(prevXSstat == 0 && currXSstat == 1 && count == 3)){
          current = Having3Persons;
        }
    if((prevESstat == 0 && currESstat == 1 && count == 4)||(prevXSstat == 0 && currXSstat == 1 && count == 4)){
          current = Having4Persons;
        }
    if((prevESstat == 0 && currESstat == 1 && count == 5)||(prevXSstat == 0 && currXSstat == 1 && count == 5)){
          current = Having5Persons;
        }
    if((prevESstat == 0 && currESstat == 1 && count == 6)||(prevXSstat == 0 && currXSstat == 1 && count == 6)){
          current = Having6Persons;
        }
    if((prevESstat == 0 && currESstat == 1 && count == 7)||(prevXSstat == 0 && currXSstat == 1 && count == 7)){
          current = Having7Persons;
        }
    if((prevESstat == 0 && currESstat == 1 && count == 8)||(prevXSstat == 0 && currXSstat == 1 && count == 8)){
          current = Having8Persons;
        }
    if((prevESstat == 0 && currESstat == 1 && count > 8)||(prevXSstat == 0 && currXSstat == 1 && count > 8)){
          current = TooManyOff1;
        }
    break;
    case Having1Person:
    Serial.println("Having1Person"
    output(1,0,0,0,0,0,0,0);
    delay(100);
    current = Counting;
    break;
      case Having2Persons:
    Serial.println("
    output(1,1,0,0,0,0,0,0);
    delay(100);
    current = Counting;
break;
  case Having3Persons:
    Serial.println("
    output(1,1,1,0,0,0,0,0);
    delay(100);
    current = Counting;
break;
    case Having4Persons:
    Serial.println("
    output(1,1,1,1,0,0,0,0);
    delay(100);
    current = Counting;
break;
    case Having5Persons:
    Serial.println("
    output(1,1,1,1,1,0,0,0);
    delay(100);
    current = Counting;
break;
    case Having6Persons:
    Serial.println("
    output(1,1,1,1,1,1,0,0);
    delay(100);
    current = Counting;
break;
    case Having7Persons:
    Serial.println("
    output(1,1,1,1,1,1,1,0);
    delay(100);
    current = Counting;
break;
    case Having8Persons:
    Serial.println("
    output(1,1,1,1,1,1,1,1);
    delay(100);
    current = Counting;
break;
    case TooManyOff1:
    Serial.println("TooManyOff1");
    output(0,0,0,0,0,0,0,0);
    delay(500);
    current = TooManyOn1;
break;
    case TooManyOn1:
    Serial.println("TooManyOn1");
    output(1,1,1,1,1,1,1,1);
    delay(500);
    current = TooManyOff2;
break;
    case TooManyOff2:
    Serial.println("TooManyOff2");
    output(0,0,0,0,0,0,0,0);
    delay(500);
    current = TooManyOn2;
break;
    case TooManyOn2:
    Serial.println("TooManyOn2");
    output(1,1,1,1,1,1,1,1);
    delay(500);
    current = Counting;
break;
  }
  prevESstat = currESstat;
  prevXSstat = currXSstat;

}